## Slide 1: Accelerator physics
Caterina Biscari
Alba-CELLS

## Slide 2: Outlook
Introduction
Historic details
Particle beam description
Accelerators in the world
Colliders
Medical Applications
Synchrotron Light Sources
Conclusions

## Slide 3: ~30000 accelerators in the world
Chart: 
| Radiotherapy | Hadrontherapy | Ion implantation | Industrial processing | Biomedicine | Isotope production | High Energy Machines
 | 11440 | 40 | 10660 | 2340 | 1040 | 300 | 260
Driving Accelerator R&D
Generation of energetic particle beams for investigations of the structure of matter e.g. nuclear and particle physics, ion beam analytics, structural analysis in biology and chemistry, kinetics and dynamics of reactions
Generation of secondary radiation for specific reactions e.g. neutrons, photons (x-rays), positrons

## Slide 4
Of about 30,000 accelerators at work in the world today, a majority is for applications in industry.There are two major categories of industrial applications: materials processing and treatment, and materials analysis. Accelerators are also applied for environment protection, such as purifying drinking water, treating waste water, disinfecting sewage sludge and removing pollutants from flue gases. Industrial accelerators continue to evolve, in terms of new applications, qualities and capabilities, and reduction of their costs. Their impact on our society continues to grow with the potential to address key issues in economics or the society of today.
Medical accelerators account for the other 8-9000 units.
Accelerators dedicated to research complete the panorama.
The R&D is driven by high energy physics, photon and neutron production, in the quest for higher energies, higher intensities, smaller beams, new acceleration techniques
Particle accelerators are a major invention of the 20th century. In the last eight decades, they have evolved enormously and have fundamentally changed the way we live, think and work.

## Slide 5
Rutherford in 1928, during his presidential address as president of the Royal Society of England, said:
“I have long hoped for a source of positive particles more energetic than those emitted from natural radioactive substances.”
These words focused the attention of many new minds as well as encouraged others who were already working on the problem.
Rutherford was using alpha particles obtained through radiative decay to study the atom structure.
Cockcroft and Walton (Nobel in 1951) built the first high voltage electrostatic generator in 1930: 300 keV (Gamow had predicted that were needed for nuclear particles to enter the nucleus). Voltage multiplying column to go to 600 keV. Protons were accelerated and used for nuclear reactions
First Particle Accelerators
Cavendish Laboratory
1927:
directed by Rutherford

## Slide 6
Basics of accelerator physics

## Slide 7
Electromagnetic field on charged particles
ACCELERATION
BENDING & FOCUSING
Beam
Electric field

## Slide 8
Charged particles
Particle energy at rest
 | e-, e+ | p, ap
mo (kg) | 9.11 10-31 | 1.67 10-27
Eo (joule) | 8.2 10-14 | 1.5 10-10
Eo (..eV) | 0.51 MeV | 0.94 GeV
Electrons, positrons,
Protons, antiprotons,
Ions
Range of particle (kinetic) energies in accelerators:
From few KeVs to fewTeVs
1 eV = 1.602 x 10-19 joules

## Slide 9
F = acceleration =
kinetic energy increase
Is there velocity increase?
Electric fields accelerate charged particles

## Slide 10: Radiofrequency cavities, powered by klystrons or Solid State Amplifiers
Particles gain energy passing through the cavity, in phase with accelerating field. The maximum possible energy gain is given by
t
E

## Slide 11
Magnetic fields deflect charged particles
Deflection : Proportional to bending magnet and particle charge, and inversely proportional to total energy of the particle.
Magnetic rigidity
Magnetic Field (Tesla) * bending radius(m) = 3.3 * Energy(GeV)

## Slide 12
Dipoles for bending trajectories
Quadrupoles to focus trajectories on central orbit
Main magnets of an accelerator

## Slide 13
Permanent magnets
Natural magnetic materials
Elettromagnets
Iron surrounded by coils
Magnetic fields
In accelerators
Permanent magnet quadrupoles
Small dimensions
No flexibility
Electromagnetic magnets,
B tuned by current in coils

## Slide 14
Main types of accelerators

## Slide 15
Linear Accelerators : Series of accelerating cavities
Idea and first prototypes in the’30s, (drift tubes suspended in a non-conducting tube by Wideroe, Particles gaining energy in the gaps). Only low frequency rf power was available (kHz regime). Need of very long structures.
Klystrons development during World War II: high frequency rf (up to GHz)
DTL: Drift Tube Linac. Alvarez in the ‘50 developed the ‘Alvarez type’, using conducting waveguides.
Today most powerful Linacs based on SC cavities, both for e-, or p

## Slide 16
Circular accelerators
Synchrotrons
Cyclotrons
Invented by Ernest Lawrence in the ’30.
Bend and accelerate with constant revolution frequency.
Nuclear physics, particle therapy,..
M. Oliphant, in the forties, joined three ideas in a single concept: the sinchrotron. Accelerate with rf cavities, change the frequency, pulse the magnets.
First synchrotron was built in UK, in Woolwich Arsenal Research Laboratory
Most actual HE physics, Synchrotron lights sources

## Slide 17: Particle beams
Beams are grouped in bunches travelling along the vacuum chambers
Every bunch contains billions of particles (N =109 – 1011)

## Slide 18: Beam description
Particles in the bunch have different positions and energies
Energy, longitudinal position, transverse position and momentum have usually gaussian distributions
The bunch can be described as an ellipsoid in 6 dimensions
Longitudinal position- Energy
Vertical position and momentum
Horizontal position and momentum
s
y
x
X
X’

## Slide 19: Beam phase space in each plane
Ellipse area = Invariant if no dissipative forces are present
Twiss parameters define orientation and form of the ellipse, the emittance its area, a, b, g vary along the accelerator

## Slide 20
The volume occupied in the phase space of a system of particles is constant in the presence of conservative forces
Liouville’s theorem
The emittance is measured in m rad (position – divergence)
Phase space in different positions along the accelerator
Low beta position
High beta position
Magnetic field acting on the beam do not modify the emittance, but modify the phase space orientation

## Slide 21: BEAM DYNAMICS DESCRIPTION
Matrix formalism
Vector of
Particle coordinates
Drift, quadrupole, bending,…
The way the particle coordinates change when passing through an element is described by the element matrix, which contains its characteristics
The accelerator is described by the product of its element matrices

## Slide 22
Matrix formalism is also used to describe Twiss Parameters behaviour along an accelerator
For the design, the simulation, the control, standard codes are used by researchers in all accelerator-based laboratories
Example of Twiss Parameter behaviour in a section of a synchrotron

## Slide 23
Synchrotron radiation
A charged particle in a magnetic field emits photons, whose energy spectrum depends on the particle mass and energy, and on the magnetic field.
The particle looses energy. In a synchrotron the energy loss is compensated by rf cavities
Energy emitted per turn
rf cavity
Lighter particles emit more energy. Electrons and positrons used as photon sources.
Bending radius – related to B
Particle rest mass

## Slide 24: Synchrotron radiation emission
 | particle | r (m) | E (GeV) | DE/turn = U (MeV)
DAFNE | e- e+ | 1.4 | 0.51 | 0.004
ALBA | e- | 7.1 | 3.0 | 1.0
LEP | e- e+ | 3026 | 100 | 2923
LHC | p | 2812 | 7000 | 12.2
Energy lost per turn

## Slide 25: Synchrotron radiation emission as a function of the beam energy
No dependence on the energy at longer wavelengths
Notes: ;

## Slide 26: Examples
Colliders – LHC, LC
Medical applications – CNAO
Synchrotron Light sources - ALBA

## Slide 27
Collider energies
Leptons
Hadrons
Hadron-Lepton

## Slide 28
Collider luminosities
Leptons
Hadrons
Hadron-Lepton

## Slide 29
Luminosity versus Energy
Leptons
Hadrons
Hadron-Lepton

## Slide 30
RHIC
DAFNE
Tau-Charm
VEPP 4M
VEPP 2000
SUPER KEK-B
In operation
In construction
LHC
Hadrons
Leptons
Leptons-Hadrons
Particle Colliders - 2013

## Slide 31: Luminosity in a collider
High luminosity:
High intensity + small beams

## Slide 32
LHC

## Slide 34
LHC complex

## Slide 35
  LHC arc view
27 km cooled down to 2K
The coolest place in the world

## Slide 36
1232 dipoles
392 quadrupoles
6200 correctors
LHC arc
Magnets

## Slide 37
Pipe for He transport and recovery
(26 km)
Helium bath at 1.9K (-271° C)
LHC arc:
Cryogenic

## Slide 38
Vacuum system for cryogenic pipes
Regular arc:
Vacuum
Vacuum system for cryostats
Vacuum chamber for the two beams
LHC arc:
Vacuum

## Slide 39
Regular arc:
Electronics
Many thousands of electronic units to control
Quench, correction, beam diagnostics, vacuum, cryogenics,…
LHC arc:
Electronics

## Slide 40: Lowering of First Dipole Magnet - 7 March 2005
A single point to lower dipoles, 15 m long and 35 Tons weight
Notes: Es gibt nur einen Schacht, inn dem die Magnete in den LHC Tunnel abgesenkt werden koennen, aufgrund der Laenge von ueber 15m.

## Slide 41: Lowering of Last Dipole Magnet 26 April 2007
~ 1700 cryo-magnets assemblies
  1232 Main Dipoles
  474 Short Straight Sections
  16 Separation Dipoles
  32 Low β Triplets
~ 200 warm magnets

## Slide 42
Tunnel
Filled with SC magnets, rf cavities,
Diagnostics and

## Slide 43
ATLAS Experiment at CERN
Experiment

## Slide 44: Evolution of LHC Luminosity
4th July
Peak Luminosity
7e33 cm-2 sec-1
Lpeak = 7.8 1033 cm-2 sec-1
4 July
Announcement on HIGGS

## Slide 45
What’s next?

## Slide 46
X 24000

## Slide 47: HIGH FIELD MAGNETS
SLHC
Higher L
1035
LHC upgrades
DLHC
Double energy
Ecm = 28 T
Low b quads
Dipoles

## Slide 48
R&D started in view of VLHC and ITER - Multi Labs and Industrial Collaborations
examples: LARP – BNL-FNAL-LBNL-SLAC (prototype for 2012)
FRESCA - EuCARD WP7 – 12 Institutes - main involvement from CERN, FERMILAB, LBNL, BNL, KEK
R&D on high field SC magnets
NbTi
Robust, ductile, well extablished and used techology
B < 10 T
Nb3Sn
Heat treatment, brittleness
B < 15 T
HTS
B up to 45 T
To be used in HL-LHC
R&D on wires , still long road for High fields magnets
Challenges: Mechanical weakness, unit length, quench detection and protection
Nb3AL
KEK, Hitachi
Subscale Magnet for demonstration (B = 13 T)
Cable production advanced

## Slide 49
Nb3Sn performance is influenced by mechanical stress and strain: brittle if > 15 T
>20T : HTS, fundamental and costly R&D, limited unit length
2012
45 T
Nakamoto, IPAC12
Plot maintained by Peter Lee at: http://magnet.fsu.edu/~lee/plot/plot.htm

## Slide 50: Future colliders – HEP community discussion
HE-LHC (High Energy LHC)
Increasing proton energy beyond 7 TeV:
(2010: study group and workshop)
reuse of the CERN infrastructure
“ease” in producing luminosity with proton circular collider
practical and technical experience gained with LHC
Beam energy set by SC magnets dipole field:
16-20 T == 26 to 33 TeV in the centre of mass.

## Slide 51
Lepton colliders

## Slide 52: e+/e- Linear Colliders CLIC and ILC
http://project-clic-cdr.web.cern.ch/project-CLIC-CDR/CDR_Volume1.pdf
http://www.linearcollider.org/cms/

## Slide 53
Dual beam acceleration technology
R&D at CERN ~ 25 y
Normal conducting cavities
12 GHz, 100 MV/m
Maximum energy 3 TeV cm – Phase I at 0.5 TeV
International collaboration around CTF3
Well extablished SC rf technology (TESLA, FLASH, EXFEL…)
2004: decision on technology for next linear collider up to 1 TeV
1.3 GHz, 31.5 MV/m
Maximum energy 1 TeV cm - Phase I at 0.5 TeV
GDE (Global Design Effort) - International collaboration
Site independent
ILC CLIC

## Slide 54: Gradient Range Yield Gain
+~15%

## Slide 55: TBTS: Two Beam Test Stand
Consistency between
produced power
drive beam current
test beam acceleration
Maximum gradient 145 MV/m
CTF3 team
TD24

## Slide 56
Nominal performance of Accelerating Structures
Design@CERN, Built/Tested @KEK, SLAC
CLIC
target
KEK
SLAC

## Slide 57
ILC layout

## Slide 58
CLIC layout
DRIVE BEAM COMPLEX
MAIN BEAM COMPLEX
QUAD
QUAD
POWER EXTRACTION
STRUCTURE
BPM
ACCELERATING
STRUCTURES

## Slide 59
Beyond HE-LHC : new tunnels in Geneve area
47 km – 80 km
1) 42 TeV c.o.m. with 8.3 T (present LHC dipoles)
2) 80 TeV c.o.m. with 16 T (high field based on Nb3Sn)
3) 100 TeV c.o.m with 20 T (very high field based on HTS)

## Slide 60
Hadron therapy facilities

## Slide 61
CA., UCSF
CA., LLUMC
IN Bloomington
TX Houston
FL, Jacksonville
Moscow
St. Petersburg
Dubna
Wanjie (WPTC)
Ilsan, Korea
Clatterbridge, Uppsala
Nice (CAL) , Orsay (CPO)
Berlin (HMI) Munich
Villigen PSI
Catania LNS since 2002
Darmstadt (GSI)
Kashiwa (NCC)
Hyogo (HIBMC)
WERC Shizuoka
Hyogo (HIBMC)
Chiba (HIMAC)
Gunma
South Africa iThemba LABS
Vancouver (TRIUMF)
> 70000 patients treated with protons
Hadrontherapy in the world
> 7000 with carbon ions
CNAO
IMP (Langzhou)

## Slide 62
Hadrontherapy first proposed by R. Wilson in 1946
In 1954: 30 patients treated with protons at LBL (Lawrence Berkeley Laboratory)
In the next years other treatments in other research centers were performed
(Uppsala, Harvard, Dubna, St.Petersburg, Moscow, PSI, Chiba, Tsukuba)
In 1990 the first dedicated hospital facility has started treatments at Loma Linda (LLUMC)

## Slide 63: Cancer therapy: X-rays
1937: first X-rays irradiation from van de Graaff electrostatic machine
1956 : first patient treated with radiotherapy at Stanford – eye tumor
Since then 40 millions patients have been treated
Today 50% of cancer patients are X-ray treated, either alone (25%) or in combination with other techniques.
Electron Linacs (4 – 22 MeV) produce e- to be shot on a metallic target and produce X-rays
Commercially produced
Thousands of compact and fully reliable Linacs are daily treating patients in all the world
Control of radiation dose and radiation fields decrease collateral effects

## Slide 64: Radiotherapy and hadrontherapy
Hadrontherapy uses hadrons (protons and heavy ions) – Bragg peak
Very localized depth-dose deposition

## Slide 65: Macroscopic advantage of hadrons
Rapid fall-off
X rays
protons

## Slide 66: Accelerator design criteria for hadrontherapy
The kind of the accelerator depends mainly on:
The species to be accelerated
The radiation shaping and delivery method
particle | Penetration range | Energy range | Brho range
Proton | 30-300 mm | 60-250 MeV/u | 1.16-2.31 Tm
Carbon | 30-300 mm | 120-400 MeV/u | 3.18-6.34 Tm
Active Scanning
Passive Scanning

## Slide 67
CNAO synchrotron hall

## Slide 68: CNAO - Accelerator and Treatement Rooms
Davide Bianculli

## Slide 69: Orders of magnitude
Treatment session duration: 30 min
Irradiation duration: 3 min
Slice thickness: 2 – 4 mm
Spot size: 4 - 10 mm
Position precision: 0.1 mm
Energy precision: 10-4
Spot duration: 5 - 10 ms
Beam current: 0.1 - 1 nA
Measurement time: < 100 ms
Dose uniformity required: ± 2.5%

## Slide 70
X-ray Patient Verification System (PVS)
2 X-ray tubes (deployable) ,
2 flat panels (deployable)
Supporting structure rotation: ±180°
Rotation and deployment accuracy: ± 0.15mm, ± 0.1°
Patient Positioning System (PPS)
Automatic couch or chair docking
Absolute accuracy: ≈ 0.3 mm
3D Real-time IR Optical Tracking (OTS)
Real time reconstruction of spherical markers and surfaces
Sub-millimeter accuracy : peak 3D errors <0.5 mm
3D data flow @70 Hz
Markers, low density fixation materials

## Slide 71: CNAO medical activity
1st patient protons: September 2011
1st patient Carbon Ions: September 2012
Three treatment rooms operational
62 Patients treated with protons
62 treated with Carbon ions
Chart: Distribuzione geografica dei pazienti del CNAO 22 Settembre 2011 – 26 Luglio 2013 Totale 124 pazienti
| Abruzzo | Basilicata | Calabria | Campania | Emilia Romagna | Lazio | Liguria | Lombardia | Marche | Piemonte | Puglia | Sardegna | Sicilia | Toscana | Veneto
Ioni Carbonio | 1 | 1 | 2 | 7 | 8 | 5 | 15 | 5 | 2 | 3 | 6 | 5
Protoni | 1 | 1 | 1 | 3 | 4 | 6 | 4 | 14 | 2 | 7 | 6 | 1 | 2 | 6 | 3
Cranium chordome and chondrosarcoma
Sacral chordome and chondrosarcoma
Intracranial meningioma
Salivary glands carcinoma
Trunk sarcoma
Prostate carcinoma
Aero-digestive mucosae melanoma

## Slide 72: Hadrontherapy history: Rapid Growth. doubled in last decade
10000
20000
40000
30000
50000
60000
70000
80000
0
1950
1960
1970
1980
1990
2000
2012
.
.
.
5
10
15
20
25
30
35
40
.
.
.
.
.
.
.
.
.
.
.
.
Centres
Patients

## Slide 73
E = hn
The higher the photon energy, the shorter the wavelength, the higher the resolution
Photon
factories

## Slide 74
Synchrotron radiation facilities in the world > 50
High brilliance and flux (combined with high collimation)
Wavelength tunability
Polarization (linear, elliptical or circular)
Time structure
Collimated (partially) coherent radiation

## Slide 75
3 Generations of Light Sources
1970s : 1st Generation – HEP rings used parasitically for X-ray production
1980s : 2nd Generation – Many dedicated X-ray sources
1990s: 3rd Generation – Several radiaiton facilities with wigglers, undulators, high brilliance
2000s: 4th Generation – Free Electron Lasers driven by Linacs
ALBA
Light source brilliance
photons/s/mm2/mr2/0.1%BW
photons per time, space, energy definition

## Slide 76
XFEL – 4th generation

## Slide 77
H. Braun

## Slide 78
ALBA, the Spanish 3rd Generation Light Source

## Slide 79
Accelerator layout
Linac
Booster
Synchrotron

## Slide 80
ALBA accelerators
 | Storage Ring | Booster Extraction
Beam Energy | 3 GeV | 3 GeV
Natural Hor Emittance | 4.6 nm*rad | 9 nm*rad
Tunes (h / v) | 18.15 / 8.36 | 12.42 / 7.38
Natural Chromaticity (h / v) | (- 40.0 / -25.6) | (-17.0 / -9.6)
Momentum Compaction Factor | 0.88 x 10-3 | 3.6 x 10-3
Energy Spread | 1.05 x 10-3 | 0.96 x 10-3
Revolution Time | 896 ns | 832 ns
Damping Times (h / v / l) | (4.6 / 8.0 / 6.4) ms | (4.6 / 8.0 / 6.4) ms
Partition Numbers (h / v / l) | (1.3 / 1.0 / 1.7) | (1.75 / 1.0 / 1.25)
Energy Loss per Turn (no IDs) | 1.2 MeV | 0.625 MeV
Harmonic Number | 448 | 416
ALBA Storage ring and Booster main parameters

## Slide 81
Material Science & Powder Diffraction
MSPD: HR & HP
Photoemission
Spectroscopy and Microscopy
CIRCE: PEEM & NAPP
Soft X-Ray
Microscopy
MISTRAL
Macromolecular
Cristallography
XALOC
Core Level Absorption and Emission
Spectroscopy
CLAESS
Phase I Instruments in ALBA
Non cristalline
Diffraction
NCD
Resonant Absortion and Scattering
BOREAS: Hector & MARES

## Slide 82: 2012 and 2013 proposal nationality
Chart: 
| FINLAND | FRANCE | GERMANY | GREECE | ITALY | NETHERLANDS | NORWAY | POLAND | PORTUGAL | RUSSIAN FEDERATION | SERBIA AND MONTENEGRO | SLOVAKIA | SPAIN | SWEDEN | TAIWAN | UKRAINE | UNITED KINGDOM | UNITED STATES
 | 2 | 6 | 31 | 12 | 34 | 5 | 1 | 4 | 11 | 5 | 6 | 4 | 467 | 1 | 2 | 1 | 9 | 2
Chart: 
| AUSTRIA | BELGIUM | DENMARK | FRANCE | GERMANY | GREECE | ITALY | POLAND | PORTUGAL | SPAIN | SWEDEN | TAIWAN | TURKEY | UNITED KINGDOM | UNITED STATES
 | 1 | 2 | 1 | 4 | 10 | 1 | 5 | 2 | 3 | 167 | 1 | 1 | 1 | 3 | 1
 | 2 | 6 | 31 | 12 | 34 | 5 | 1 | 4 | 11 | 5 | 6 | 4 | 467 | 1 | 2 | 1 | 9 | 2
2012
2013
Average Overbooking factor: ~ 2
Industrial Users start to use the facility

## Slide 83
One of ALBA Beamlines (CIRCE)

## Slide 84
Protein resolved in the
XALOC Beamline at ALBA

## Slide 85: Accelerator physics is not only Maxwell and Lorentz equations
Vlasov equation
Hill equation
Schoedinger equation
CONTROLS & COMPUTERS
Advanced Electronics
Genetic algorithms
Simplectic codes
Vacuum technology
Laser technology
Plasma Physics
Hamiltonian treatment
Landau damping
Impedances
Feedback systems
Simulation codes
Conventional cooling and electrical systems
Beam instrumentation
Cryogenics
Statistical and collective effects

## Slide 86: History: Andrew Sessler and Edmund Wilson –”Engines of Discovery”, World Scientific Editors Accelerator physics: CAS (Cern Accelerator School) proceedings - http://cas.web.cern.ch/cas/ USPAS (US Particle Accelerator School) - http://uspas.fnal.gov/course-materials/most-recent-school.shtml Recent papers on accelerators Joachim Stohr - The Scientific Revolution Enabled by X-ray Free Electron Lasers – IPAC 12 Conference Proceedings Mats Lindros – European Startegy Group Symposium Caterina Biscari – European Strategy Group Symposium Hans Braun - The Future of Xray FELs Mike Lamont – The first years of LHC Operation for Luminosity Production Sandro Rossi - http://link.springer.com/article/10.1140%2Fepjp%2Fi2011-11078-8#page-1
Some references