## Slide 1
INTRODUCTION TO SUPERCONDUCTING QUBITS
From
Fundamentals
to
Practical Modeling
Jens Koch Northwestern University
Jens Koch
Dept. of Physics & Astronomy Northwestern University
Spring School on Superconducting Qubit Technology Benasque 2023

## Slide 2
circuit quantization
introduction a short conceptual
overview
1
2
3
transmon & fluxonium

## Slide 3
1
introduction a short conceptual
overview

## Slide 4
Questions for the experienced & restless:
How does the offset charge ng enter the classical equations of motion of the Cooper pair box/transmon?
The Cooper pair box/transmon Hamiltonian looks like that of a fictitious particle in a 1d periodic potential. Yet, eigenstates are different here from the Bloch waves of a 1d crystal. How so & why?

## Slide 5
atoms ions
NV centers
spins
photons
quantum computing
hardware
superconducting circuits
and cavities

## Slide 6
C
L
energy dissipation,
interaction with the environment inevitable
dramatically reduces quantum effects
Building quantum bits from circuits

## Slide 7
Building quantum bits from superconducting circuits
L
C

## Slide 8
superconductor
Building quantum bits from superconducting circuits
► dissipationless (no Ohmic resistance)
► provides nonlinearity via Josephson effect
► OK to use dirty materials
E
2D ~ 1 meV
superconducting gap
“forest” of
states

## Slide 9
Building quantum bits from superconducting circuits
■ discrete energy levels
■ anharmonic spectrum
■ coupling to EM field

## Slide 11
++++
- - - -
Q
Ф
charging
energy
inductive
energy

## Slide 13
not a good qubit… need nonlinearity
Quantum
LC oscillator as a qubit?

## Slide 17: From LC oscillator to transmon
Introduce nonlinearity: replace inductor with
Josephson junction

## Slide 18: Transmon qubit
Nb
sapphire
Al
AlOx Al

## Slide 19
TRANSMON
T
R
A
N
S
M
O
N
~ 2007

## Slide 20
https://www.transmon.co.uk/
established in 1996, Transmon Engineering Ltd has remained at the forefront of the forklift and materials handling sector

## Slide 21
1/f charge noise
1/f flux noise
critical current noise
dielectric loss
photon shot noise
Purcell decay
nonequilibrium quasiparticles
…
QUBIT
DECOHERENCE
/ ERRORS
Your qubit ran into a problem that it couldn’t handle, and now it needs to restart.
HBAR_DIED_A_HORRIBLE_DEATH
noise
Notes: Until quantum error correction is in place, we care about noise and ways to mitigate it. No qubit is ever alone in the universe. Every qubit couples - hopefully weakly – to uncontrolled degrees of freedom in the environment. For superconducting qubits, a variety of important noise channels are known (though not necessarily well understood in their microscopic origin).
The presence of noise reduces gate fidelities and ultimately leads to errors in the execution of a quantum algorithm. So without some strategy for handling errors, a future quantum computer will keep crashing with a blue screen like this: …
To try and rescue hbar from this horrible death, it is helpful to remember and distinguish the two primary modes of decoherence – so allow me to run through a very quick recap.

## Slide 22
…
reduce noise (materials science, fabrication, microwave engineering, …)
active quantum error correction (monitor for errors, apply correction steps when required in feedback loop)
intrinsic noise protection (develop circuits that are insensitive to noise)



error mitigation strategies

## Slide 23
1/f noise
charge noise Cooper pair box
flux noise rf SQUID qubit, 3-junction flux qubit

## Slide 24
Cooper pair box

## Slide 25
V Bouchiat et al., Phys. Scr. 1998, 165 (1998)
Cooper pair box

## Slide 26
energy
ng
► dephasing
charge noise
dephasing

## Slide 27: Flattening the spectrum for charge noise protection
energy
ng
increase EJ / EC
energy
ng
energy
ng

## Slide 28
2
circuit quantization from circuit diagram to Hamiltonian

## Slide 36
node variables, branch variables, “collective” variables
external magnetic flux & loop constraints (Kirchhoff’s voltage law & flux quantization)
periodic vs. extended degrees of freedom (boundary conditions matter!)
free (cyclic) and frozen modes
automating circuit quantization (scqubits.Circuit)
circuit quantization for time-dependent magn. flux
circuit quantization
introduction a short conceptual
overview
noise, decoherence & noise protection
composite circuit QED systems
transmon & fluxonium
1
2
3
4
5

## Slide 37: Josephson effect
superconductor
superconductor
insulator

## Slide 38: Circuit elements
circuit element | constitutive relation | energy

## Slide 39: Circuit elements
circuit element | constitutive relation | energy

## Slide 40: Circuit elements
circuit element | constitutive relation | energy
“generalized flux” variables
➙

## Slide 41
circuit quantization
introduction a short conceptual
overview
noise, decoherence & noise protection
composite circuit QED systems
1
2
4
5
charge regime (CPB) vs. transmon regime
charge dispersion and anharmonicity
effective model for low-lying levels (Taylor expansion of cosine)
insensitivity to dc offset charge
plasmon vs. fluxon transitions
heavy fluxonium, blochnium
transmon & fluxonium
3
transmon
fluxonium

## Slide 42
circuit quantization
introduction a short conceptual
overview
noise, decoherence & noise protection
composite circuit QED systems
1
2
4
5
transmon & fluxonium
3
T1 depolarization (relaxation & excitation) protection via localization/disjoint support
Tφ pure dephasing protection via “flattening” energy levels
circuits with simultaneous protection, e.g. 0-pi circuit

## Slide 43
circuit quantization
introduction a short conceptual
overview
noise, decoherence & noise protection
composite circuit QED systems
1
2
4
5
transmon & fluxonium
3
dispersive regime
readout and control
interfacing scqubits/QuTiP for simulating time dynamics

## Slide 44
2021
2022
2020
# downloads via conda
121,130
2023
19 releases
>2,000 commits
>29,000 lines of code
2 papers
URL: tiny.cc/qubit
Open source ( BSD license)
Air Force Office for
Scientific Research
FA9550-20-1-0271
Superconducting Qubits in Python

## Slide 45
docs: tiny.cc/qubit
INSTALL
conda install –c conda-forge scqubits
pip install scqubits

## Slide 46
tinyurl.com/bnsq2023
Companion jupyter notebook:

## Slide 47
Hamiltonian
?
Devoret (1997) Quantum Fluctuations in Electrical Circuits Quantum Fluctuations, Les Houches, Session LXIII
Vool & Devoret, Int. J. Circ. Theor. Appl. 45 897–934 (2017)
Burkard, Koch, and DiVincenzo, Phys. Rev. B 69 064503 (2004)
circuit quantization (cont’d)

## Slide 48
circuit analysis: variable classification

## Slide 49: Kirchhoff’s loop rule and magnetic flux
×
×
Kirchhoff’s voltage law for loop:

## Slide 50
circuit quantization

## Slide 51
scqubits
custom circuit analysis,
quantization & solver
toy example: zero-pi
zp_yaml = """
branches:
- [JJ, 1, 2, EJ = 10, 20]
- [JJ, 3, 4, EJ, 20]
- [L, 2, 3, 0.008]
- [L, 4, 1, 0.008]
- [C, 1, 3, 0.02]
- [C, 2, 4, 0.02]
"""

## Slide 52
scqubits
custom circuit analysis,
quantization & solver

## Slide 53
scqubits
custom circuit analysis,
quantization & solver

## Slide 54
scqubits
custom circuit analysis,
quantization & solver
composite systems of custom and known circuits
multi-dim. parameter sweeps
lots of visualization routines
[noise: upcoming release]
offset charges
ext. flux